SAFETY DATA SHEET

1. PRODUCT NAME:             1104 SOLVENT  (THINNER/CLEANER)

2. COMPOSITION/INFORMATION ON INGREDIENTS:

Name                                           Conc Range   Symbol    Risk Phrase*

ETHOXY PROPANOL                >50%               Xi         FR10-36

BUTYL DIGYCOL                      5-10%              Xi             R36

*for full text see section 16

3.HAZARDS IDENTIFICATION:

Flammable, irritant

4. FIRST AID MEASURES:

GENERAL:              In all cases of doubt, or when symptoms persist, seek medical attention.

Never give anything by mouth to an unconscious person.

INHALATION:       Remove to fresh air, keep patient warm and at rest. If breathing is irregular or stopped

administer artificial respiration. Give nothing by mouth if unconscious place in the

recovery position and seek medical advice.

SKIN CONTACT:   Remove contaminated clothing. Wash skin thoroughly with soap and water or

recognised skin cleaner.

EYE CONTACT:    Contact lenses should be removed. Irrigate copiously with clean fresh water for at least

10 minutes, holding the eyelids apart and seek medical advice.

INGESTION:          If accidentally swallowed obtain immediate medical attention. Keep at rest. Do not

induce vomiting. Do not give anything by mouth to an unconscious person.

5. FIRE FIGHTING MEASURES:

Extinguishing Media:

Recommended:            Alcohol resistant foam. CO2 power. Water spray/mist

Not to be used:             Water jet.

Recommendations:

Fire will produce dense black smoke containing hazardous products of combustion (see Section 10).

Decomposition products may be a hazard to health. Appropriate self-contained breathing apparatus may be required. Cool closed containers exposed to fire with water spray. Do not all run-off from fire fighting to enter drains or water courses.

6. ACCIDENTAL RELEASE MEASURES:

Exclude non-essential personnel. Avoid breathing vapours. Refer to protective measures listed in sections 7 and 8. Contain and collect spillages with non-combustible absorbent materials, e.g. sand, earth, vermiculite, diatomaceous earth and plate in a suitable container for disposal in accordance with the waste regulations (see section 13). Do not allow to enter drains or water courses. If the product enters the drains or sewers the local Water Company should be contacted immediately, in case of contamination of streams, rivers or lakes, the National Rivers Authority. Clean preferably with a detergent: avoid the use of solvents.

7. HANDLING AND STORAGE

Handling:

Prevent airborne concentrations higher than the occupational exposure limits. Keep the container tightly closed.  Exclude sources o heat, sparks and open flame. Avoid skin and eye contact. Avoid inhalation of vapour and spray mist. Smoking, eating and drinking should be prohibited in areas of storage and use. For personal protection see Section 8.

Unless the container is specifically designed, never use pressure to empty, it is nor a pressure vessel.

Always keep containers made of the same material as the supply container.

Good housekeeping standards and regular removal of waste materials will minimise risk of spontaneous combustion and other fire hazards.

The Manual Handling Regulations may apply to the

8. EXPOSURE CONTROLS/PERSONAL PROTECTION